## Slide 1: Downscaling European decarbonization scenarios of the heating sector to the Austrian community level
Assessing the heat density gap of centralized heat networks between 2050 and today
Young Scientist Summer Program 2021 Final colloquium presentation 21/08/25
Corresponding author/Presenter: zwickl@eeg.tuwien.ac.at https://github.com/sebastianzwickl
Sebastian Zwickl-Bernhard1, Daniel Huppmann2
1Energy Economics Group (EEG), Technische Universität Wien
2International Institute for Applied Systems Analysis

## Slide 2: The scope of changes in the European heating sector
The average share of renewables in the heating & cooling sector is only just above on average in all EU member states1
In Austria it is - but fossil fuels continue to dominant the provision of heating and cooling services here as well
dwellings are heated with natural gas and with oil (Austria 2020)
Retrofitting of appliances per year, or more than per day since the viability of green gas is uncertain at the end-user device level2
Requires to a massive expansion of centralized heating (and cooling) networks to…
  …ensure a highly efficient usage of renewable heat sources (e.g., biomass/waste, hydrogen)
  …achieve significant retrofitting rates by high connection rates
  …unburden the electricity sector (high electrification of different energy service needs)
1Eurostat https://ec.europa.eu/eurostat/web/products-eurostat-news/-/ddn-20200211-1
2Zwickl-Bernhard & Auer, Energy, (2021). doi: 10.1016/j.energy.2021.121805
Notes: I start this presentation with a brief overview of the European heating sector. So far, fossil-fuel based heat generation dominates the supply of heat service needs. The share of renewable energy in the provision of heating and cooling services is only just above 20% on average in all EU member states. In Austria, it is 34%. However, fossil fuels continue to dominant here as well. To be more precise, 1.4 million dwellings are heated with natural gas or oil in Austria today. Switching these heating systems to renewable energy by 2050, retrofitting 50 thousand end-user devices per year or more than 130 per day becomes necessary. To achieve this goal, we need not only sustainable decentralized heating systems, but also a massive expansion of centralized heating and cooling networks. In particular, district heating networks will play a crucial role as they (i) ensure a highly efficient usage of renewable heat sources, such as biomass/waste and hydrogen; (ii) give us the opportunity to achieve significant retrofitting rates by high connection rates; and (iii) can unburden the electricity sector as we expect high electrification rates of different energy service needs, such as in the transport and industry sector.

## Slide 3: The core objective of this work
The core objective is the downscaling of decarbonization scenarios1 of the heating sector, taking into account the infrastructure/network requirements of heat generation technologies/sources, from the country to the community level.
In particular, the prioritized preference of heat sources in centralized heat networks plays a crucial role, ensuring highly efficient usage of heat sources.
The assessment of centralized heat networks using heat density as a criterion is important in this analysis.
An Austrian case study is conducted, downscaling cost-minimizing heat generation portfolios , obtained from the large numerical energy system model GENeSYS-MOD2, from the country to the grid level.
1Developed in the European H2020 project openENTRANCE aiming for the 1.5/2.0°C global warming climate target
2Löffler et al., Energies, (2017). doi: 10.3390/en10101468
Notes: Against this background, the core objective of this work is the downscaling of decarbonization scenarios of the heating sector, taking into account the infrastructure/network requirements of heat generation technologies/sources, from the country to the community level. In particular, the prioritized preference of heat sources in centralized heat networks plays a crucial role, ensuring highly efficient usage of heat sources. Moreover, the assessment of centralized or district heating networks using heat density as a criterion is important in this analysis. We conduct an Austrian case study, downscaling cost-minimizing heat generation portfolios 2050, obtained from the large numerical energy system model GENeSYS-MOD, from the country to the grid level.

## Slide 4: Methodology
Three different scenario-independent downscaling techniques
  Proportional downscaling using population as a proxy (NUTS0 to the LAU level)
  Sequential downscaling algorithm using population density and infrastructure requirements of heat technologies/sources as additional criterion (NUTS0 to the NUTS3)
  Iterative downscaling algorithm based on graph-theory benchmarking (NUTS3 to the LAU level)
Spatial levels
The Nomenclature of Territorial Units for Statistics (NUTS) were created by Eurostat in order to define territorial units for the production of regional statistics across the European Union.
Reference technique
Techniques developed
Notes: Here, the applied methodology is briefly explained. First, as we focus here on spatial downscaling, we have to define different spatial levels. Therefore, we use the Nomenclature of Territorial Units for Statistics (NUTS) for different spatial granularities. The table at the top shows the different NUTS classifications and some examples for Austria. For example NUTS0 corresponds to the country level. In our study, we use the three gray-marked NUTS classifications NUTS0, NUTS3 and LAU. An example for a NUTS3 region in Austria is the area Linz-Wels in Upper Austria and includes a population of around 500 thousand people. The LAU level represents small communities, for example the area of Enns with a population of 11 thousand. The country of Austria is split into more than 2 thousand of those communities. We use three different scenario-independent downscaling techniques. First, proportional downscaling, using population as a proxy as a reference and well-established downscaling technique. Second, a sequential downscaling algorithm, using population density and infrastructure requirements of heat sources as a criterion and an iterative downscaling algorithm, which bases on graph-theory benchmarking.

## Slide 5: Numerical example and scenarios
Four different decarbonization scenarios of the European energy system aiming for the 1.5/2.0°C global warming climate target1
  Directed Transition scenario (strong policy incentives)
  Societal Commitment scenario (strong societal acceptance, decentralized renewables)
  Techno-Friendly scenario (market-driven breakthrough of renewables)
  Gradual Development scenario (“little of each”)
Values of the decarbonized heating sector in Austria 2050 obtained by the large-numerical energy system model GENeSYS-MOD
1Scenario a) to c) considers the 1.5°C global warming target and d) the less ambitious 2.0°C.
2050
c) Techno-Friendly
Notes: We analyze four different decarbonization scenarios of the European energy system considering the 1.5/2°C climate targets. The scenarios are developed in the H2020 project openENTRANCE and cover a wide range of future developments and uncertainties. The four scenarios are named: Directed Transition, Societal Commitment, Techno-Friendly, and Gradual Development. The underlying concept of the scenarios is a three-dimensional space, whereby each scenario emphasizes a strong sustainable development of one dimension. For example, the Directed Transition scenario (a) considers strong policy incentives enabling the sustainable transition. In contrast, the Techno-friendly scenario takes into account a significant market-driven breakthrough of renewables without being dependent on energy policy measures.

## Slide 6
Notes: The following four slide present the highlights of the generated results. First, here we see the heat generation by source on different spatial levels and in the four different scenarios. The heat sources that are prioritized in the district heating network are marked by the blue edge. As you can see, those technologies only supply highly populated areas, whereby rural areas are supplied by direct electric heating, small-scale air-sourced heat pumps and heat storage. The graph on the right shows the district heating network topology. Each point represents the quantity of heat demand supplied by the network. The largest network is obtained in the Gradual development scenario at the bottom right, since this scenario considers the less ambitious 2.0°C global warming target and reduces the total heat demand less than the other scenarios.

## Slide 7
Notes: This heatmap shows the potentials of centralized heat networks 2050 in Austria. As you can see, there are centralized heat networks in six NUTS3 regions. The heat demand supplied by the district heating networks varies among the areas and scenarios between 1.5 and almost 8 TWh. The other sub-regions are supplied by decentralized heating systems as shown in the rural sub-figure on the previous slide. However, obtaining a more realistic estimate of district heating networks in the six sub-regions requires an even finer spatial granularity, as indicated by the orange box. We therefore subjected each of these 6 regions of potential to a further downscaling algorithm that provides more accurate projections of district heating networks based on graph theory benchmarking.

## Slide 8
Notes: The example of the NUTS3 region in the orange box is illustrated here. The initial condition means the supply of heat demand in all 75 communities. This large supply area results in a difficult network topology since communities are connected with low heat densities. This results in a low benchmark indicator value of the network. As you can see, our downscaling algorithm improves the network topology by reallocation of the centralized heat supply. The smaller supply area in the final condition has a higher benchmark indicator values and includes 47 communities. The improvement of the network topology results in reduction of the population connected (-13.3%) to the network, as you can see at the bottom right.

## Slide 9
http://www.austrian-heatmap.gv.at/karte/
Notes: This figure shows the heat density of the NUTS3 sub-region Graz 2050 in the Techno-Friendly scenario. As you can see by the waterfall diagram, the different downscaling techniques significantly increase the estimates of the heat density. We obtain for the specific region in the Techno-Friendly scenario a heat density of the district heating network for more than 2.5 GWh per square kilometer. However, the pink bar indicates the gap of heat density between the projection of 2050 and the today’s networks. This gap is the smallest in the Techno-Friendly, why we used this scenario here for the waterfall, and the largest in the Societal Commitment scenario. The difference of the heat density gap between the scenarios is indicated by the gray bar and the different markers.

## Slide 10: Conclusions
Downscaling values of the heating sector require more advanced techniques than proportional downscaling
Otherwise, misinterpretation of heat generation portfolios and misestimating the potentials of centralized heat networks on the local level
In particular, prioritized preferences and graph theory-based benchmarking can improve the projections of downscaled values of the heating sector
Despite improved accuracy, a significant reduction of heat densities of centralized heat networks compared to today’s networks is expected by 2050 (heat density gap)
Incentives to provide heat network infrastructure are likely be needed in areas which today would not be connected/supplied today

## Slide 11: Acknowledgments / References
Collaborators
  Daniel Huppmann (International Institute for Applied Systems Analysis)
  Antonia Golab (Energy Economics Group – Technische Universität Wien)
  Hans Auer (Energy Economics Group – Technische Universität Wien)
References
  H. Auer et al. (2020). Development and modelling of different decarbonization scenarios at the European energy system until 2050 as a contribution to achieving the ambitious 1.5°C climate target – establishment of open source/data modelling in the European H2020 project openENTRANCE, e&i Elektrotechnik und Informationstechnik, 1-13. doi: 10.1007/s00502-020-00832-7